## Slide 1: CHAPTER 1 INTRODUCTION ON COMPUTER NETWORK
ThS. Nguyễn Viết Hùng
Khoa: Công nghê thông tin
Email: hungnv@eaut.edu.vn
Web: https://nvhung278.blogspot.com/

## Slide 2: Chapter 1: ROADMAP
  What is Computer Network?
  Network edge
    end systems, access networks, links
  Network core
    packet switching, circuit switching, network structure
  Delay, loss, throughput in networks
  Protocol layers, service models
  Networks under attack: security
  History

## Slide 3: ĐỊNH NGHĨA
Mạng máy tính:
  thiết bị mạng (host, server, network devices)
  phương tiện truyền dẫn vật lý (transmission medium)
  kiến trúc mạng (network architecture)
    cấu trúc mạng (Topology)
    giao thức mạng (Protocols)

## Slide 4: What’s the Internet: a component view
wired
links
wireless links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless laptop
millions of connected computing devices:
hosts = end systems
running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate:
bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches

## Slide 5: What’s the Internet: a protocol view
Internet: “network of networks”
  Interconnected ISPs
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype,
802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task
Force
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 6: What’s the Internet: a service view
mobile network
global ISP
regional ISP
home
network
institutional
network
Infrastructure that provides services to applications:
  Web, VoIP, email, games, e- commerce, social nets, …
provides programming interface to apps
  hooks that allow sending and receiving app programs to “connect” to Internet
  provides service options, analogous to postal service

## Slide 7: What’s the Internet: goal
Chia sẻ tài nguyên dùng chung
Nâng cao độ tin cậy
Môi trường giao tiếp người – máy
Giảm chi phí đầu tư phần cứng
Bảo đảm các tiêu chuẩn thống nhất về tính bảo mật, an toàn dữ liệu

## Slide 8: Topology
Kiểu điểm - điểm (Point to Point)
Các mạng có cấu trúc điểm - điểm (Star, Ring, Tree)

## Slide 9: Topology
Kiểu đa điểm hay quảng bá (Point to Multipoint, Broadcasting)
Các mạng có cấu trúc quảng bá (Bus, Ring, and Satellite)

## Slide 10: What’s a protocol?
human protocols:
“what’s the time?”
“I have a question”
introductions
… specific msgs sent
… specific actions taken when msgs received, or other events
network protocols:
machines rather than humans
all communication activity in Internet governed by protocols
protocols define format, order of msgs sent and received among network entities, and actions taken on msg
transmission, receipt

## Slide 11: What’s a protocol?
a human protocol and a computer network
protocol:
Hi
Hi
Got the time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
Q: other human protocols?
TCP connection
request

## Slide 12: What’s a protocol?
Chức năng giao thức
  Encapsulation
  Fragmentation
  Connection control
  Monitoring
  Flow control
  Error control
  Synchronization
  Addressing

## Slide 13: Chapter 1: roadmap
  What is the Internet?
  Network edge
    End systems, access networks, links
  Network core
    Packet switching, circuit switching, network structure
  Delay, loss, throughput in networks
  Protocol layers, service models
  Networks under attack: security
  History

## Slide 14: A closer look at network structure
network edge:
  hosts: clients and servers
  servers often in data centers
access networks, physical media: wired, wireless communication links
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 15: Access networks and physical media
Q: How to connect end systems to edge router?
residential access nets
institutional access networks
(school, company)
mobile access networks
keep in mind:
bandwidth (bits per second) of
access network?
shared or dedicated?

## Slide 16: Access net: digital subscriber line (DSL)
central office
ISP
telephone network
DSLAM
voice, data transmitted
at different frequencies over dedicated line to central office
use existing telephone line to central office DSLAM
  data over DSL phone line goes to Internet
  voice over DSL phone line goes to telephone net
< 2.5 Mbps upstream transmission rate (typically < 1 Mbps)
< 24 Mbps downstream transmission rate (typically < 10 Mbps)
DSL
modem
splitter
DSL access multiplexer

## Slide 17: Access net: cable network
cable
modem
splitter
…
cable headend
C O
V V V V V V N
I I I I I I D D T
D D D D D A A R
E E E E E T T O O O O O O O A A L
1 2 3 4 5 6 7 8 9
Channels
frequency division multiplexing: different channels transmitted in different frequency bands
Shared cable

## Slide 18: Access net: cable network
data, TV transmitted at different
frequencies over shared cable
distribution network
cable splitter modem
…
cable headend
CMTS
ISP
cable modem termination system
HFC: hybrid fiber coax
  asymmetric: up to 30Mbps downstream transmission rate, 2 Mbps upstream transmission rate
network of cable, fiber attaches homes to ISP router
  homes share access network to cable headend
  unlike DSL, which has dedicated access to central office

## Slide 19: Access net: home network
to/from headend or central office
cable or DSL modem
router, firewall, NAT
wired Ethernet (100 Mbps)
wireless access
point (54 Mbps)
wireless devices
often combined in single box

## Slide 20: Enterprise access networks (Ethernet)
typically used in companies, universities, etc
10 Mbps, 100Mbps, 1Gbps, 10Gbps transmission rates
today, end systems typically connect into Ethernet switch
Ethernet
switch
mail,
web servers
link to
ISP (Internet)
router

## Slide 21: Wireless access networks
shared wireless access network connects end system to router
via base station aka “access point”
wireless LANs:
within building (100 ft)
802.11b/g (WiFi): 11, 54 Mbps transmission rate
wide-area wireless access
provided by telco (cellular) operator, 10’s km
between 1 and 10 Mbps
3G, 4G: LTE
to Internet
to Internet

## Slide 22: Physical media
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio

## Slide 23: Physical media: coax, fiber
twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gpbs Ethernet
  Category 6: 10Gbps
coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple channels on cable
  HFC

## Slide 24: Physical media: coax, fiber
Fiber optic cable:
Glass fiber carrying light pulses, each pulse a bit
High-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gpbs transmission rate)
Low error rate:
  repeaters spaced far apart
  immune to electromagnetic noise

## Slide 25: Physical media: radio, viba, Infrared
Signal carried in electromagnetic spectrum
No physical “wire”
Bidirectional
Bropagation environment effects:
  Reflection
  Obstruction by objects
  Interference
Radio link types:
Terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g.,WiFi)
  11Mbps, 54 Mbps
Wide-area (e.g., cellular)
  3G cellular: ~ few Mbps
Satellite
  Kbps to 45Mbps channel (or multiple smaller channels)
  270 msec end-end delay
  geosynchronous versus low altitude

## Slide 26: Chapter 1: roadmap
  What is the Internet?
  Network edge
    End systems, access networks, links
  Network core
    packet switching, circuit switching, network structure
  delay, loss, throughput in networks
  protocol layers, service models
  networks under attack: security
  history

## Slide 27: The network core
Mesh of interconnected routers
Packet-switching: hosts break application-layer messages into packets
  Forward packets from one router to the next, across links on path from source to destination
  Each packet transmitted at full link capacity

## Slide 28: Packet-switching: store-and-forward
source
destination
one-hop numerical example:
L = 7.5 Mbits
R = 1.5 Mbps
one-hop transmission delay = 5 sec
more on delay shortly …
3 2 1
L bits
per packet
R bps
R bps
takes L/R seconds to transmit (push out) L-bit packet into link at R bps
store and forward: entire packet must arrive at router before it can be transmitted on next link
end-end delay = 2L/R (assuming zero propagation delay)

## Slide 29: Packet Switching: queueing delay, loss
queuing and loss:
If arrival rate (in bits) to link exceeds transmission rate of link for a period of time:
  packets will queue, wait to be transmitted on link
  packets can be dropped (lost) if memory (buffer) fills up
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets waiting for output link

## Slide 30: Two key network-core functions
forwarding: move packets from router’s input to appropriate router output
routing: determines source- destination route taken by packets
routing algorithms
routing algorithm
local forwarding table | 
header value | output link
0100 | 3
0101 | 2
0111 | 2
1001 | 1
1
2
3
dest address in arriving packet’s header

## Slide 31: Alternative core: circuit switching
end-end resources allocated to, reserved for “call” between source & dest:
In diagram, each link has four
circuits.
  call gets 2nd circuit in top link and 1st circuit in right link.
dedicated resources: no sharing
  circuit-like (guaranteed)
performance
circuit segment idle if not used by
call (no sharing)
Commonly used in traditional telephone networks

## Slide 32: Circuit switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
Example:
4 users

## Slide 33: Phân loại mạng máy tính
Theo khoảng cách
□ Mạng cục bộ LAN (Local Area Networks)
Cấu trúc mạng hình BUS

## Slide 34: Phân loại mạng máy tính
Theo khoảng cách
Mạng cục bộ LAN (Local Area Networks)
Cấu trúc mạng hình RING

## Slide 35: Phân loại mạng máy tính
Theo khoảng cách
Mạng cục bộ LAN (Local Area Networks)
Cấu trúc mạng hình sao

## Slide 36: Phân loại mạng máy tính
Theo khoảng cách
Mạng đô thị MAN (Metropolitan Area Networks)

## Slide 37: Phân loại mạng máy tính
Theo khoảng cách
Mạng diện rộng WAN (Wide Area Networks)

## Slide 38: Phân loại mạng máy tính
Phân loại theo cơ chế chuyển mạch
Mạng chuyển mạch kênh (Circuit Switched Networks)

## Slide 39: Phân loại mạng máy tính
Phân loại theo cơ chế chuyển mạch
Mạng chuyển mạch thông báo (message-switched network)

## Slide 40: Phân loại mạng máy tính
Phân loại theo cơ chế chuyển mạch
Mạng chuyển mạch gói (Packet Switched Networks)

## Slide 41: Phân loại mạng máy tính
41
Phân loại theo cơ chế chuyển mạch
Mạng chuyển mạch gói (Packet Switched Networks)
ts1
A
R1 R2 R3
B
 | t “Store-and-Forward” at s2 |  | 
tp1 |  | ts3 | 
tp2 |  |  | ts4
each Router
tp3
tp4
n
s
i
i1 i
min(de2e )   (t p  t )
A
R1 R2 R3
B
tq1
ts1
ts2
ts3
ts4
tp1
tp2
tp3
tp4
tq2
n
d 
i1
e2e 
(t p  ts  tq )
i i i
Trong điều kiện tải cao, các gói đi vào nút mạng phải đợi trong hàng đợi trước khi được gửi ra đầu ra

## Slide 42: Phân loại mạng máy tính
Phân loại theo cơ chế chuyển mạch
So sánh các cơ chế chuyển mạch (bài tập)

## Slide 43: Phân loại mạng máy tính
Phân loại theo mô hình xử lý dữ liệu
Mô hình Client-Server
Mô hình chủ /khách (Client / Server)

## Slide 44: Phân loại mạng máy tính
Phân loại theo mô hình xử lý dữ liệu
Mô hình Client-Server

## Slide 45: Phân loại mạng máy tính
Phân loại theo mô hình xử lý dữ liệu
Mô hình Client-Server
Mô hình Client-Server nhiều lớp

## Slide 46: Phân loại mạng máy tính
Phân loại theo mô hình xử lý dữ liệu
Mô hình ngang hàng (Peer-to-Peer)

## Slide 47: Kích cỡ mạng
PAN (<10m) (IEEE802.15, ETSI HIPER PAN)
IEEE
802.3,5,11
LAN ETSI HIPERLAN
IEEE 802.4,6,16
MAN ETSI HIPERMAN
& HIPER ACCESS
WAN
IEEE 802.20
3GPP 3G, LTE
ATM

## Slide 48: Một số mạng điển hình
IEEE 802
  IEEE 802.3: Chuẩn mạng LAN/MAN – Ethernet
  IEEE 802.4: Chuẩn mạng LAN – Token Bus, chủ yếu được sử dụng trong công nghiệp)

## Slide 49: Một số mạng điển hình
IEEE 802
  IEEE 802.5: chuẩn mạng LAN – Token Ring được phát triển bởi IBM
  IEEE 802.6: chuẩn mạng MAN – DQDB (Distributed Queue Dual Bus) với tốc độ 150Mbit/s trên khoảng cách 160km

## Slide 50: Một số mạng điển hình
IEEE 802
  IEEE 802.11: chuẩn mạng LAN không dây
  IEEE 802.15: chuẩn mạng cá nhân không dây (Wireless Personal Area
Network - WPAN)
    IEEE 802.15.1: BlueTooth
    IEEE 802.15.3: High rate WPAN (11 – 55Mbit/s): sử dụng cho các ứng dụng
multimedia
    IEEE 802.15.4: Low rate WPAN/ZigBee: cho các ứng dụng tiêu thụ ít năng lượng, tốc độ thấp (Wireless Sensor Network)

## Slide 51: Một số mạng điển hình
IEEE 802
  IEEE 802.16: Chuẩn mạng WMAN – WiMAX
    IEEE 802.16-2004: WiMAX cố định
    IEEE 802.16e-2005: WiMAX di động
  IEEE 802.20: WWAN – Mobile Broadband Wireless Access (MBWA), tầm phủ sóng lớn hơn WiMAX (< 15km)

## Slide 52: Một số mạng điển hình
3GPP
  3G/HSPA (High Speed Packet Access)
  LTE (Long Term Evolution)
ATM Forum
  ATM

## Slide 53: Internet structure: network of networks
End systems connect to Internet via access ISPs (Internet Service Providers)
  Residential, company and university ISPs
Access ISPs in turn must be interconnected.
So that any two hosts can send packets to each other
Resulting network of networks is very complex
  Evolution was driven by economics and national policies
Let’s take a stepwise approach to describe current Internet structure

## Slide 54: Internet structure: network of networks
Question: given millions of access ISPs, how to connect
them together?
access net
access net
access net
access net
access net
access net
access net
access net
access net
access net
access net
access net
access net
access net
access net
access net

## Slide 55: Internet structure: network of networks
Option: connect each access ISP to every other access ISP?
access net
access net
access net
access net
access net
access net
access
net
access net
access net
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
access net
access net
access net
access net
access net
access net
access net

## Slide 56: Internet structure: network of networks
access net
access net
access net
access net
access net
access net
access net
access net
access net
Option: connect each access ISP to a global transit ISP? Customer and provider ISPs have economic agreement.
access net
access net
access net
access net
access net
access net
access net
global ISP

## Slide 57: Internet structure: network of networks
access net
access net
access
access net
access net
access net
access net
access net
access net
access net
access net
access net
But if one global ISP is viable business, there will be competitors
….
ISP B
ISP A
ISP C
net
access net
access net
access net
access net
57

## Slide 58: Internet structure: network of networks
access net
access net
access
access net
access net
access net
access net
access net
access net
access net
access net
access net
ISP B
ISP A
ISP C
IXP
IXP
peering link
But if one global ISP is viable business, there will be competitors
…. which must be interconnected
Internet exchange point
net
access net
access net
access net
access net

## Slide 59: Internet structure: network of networks
access net
access net
access
access net
access net
access net
access net
access net
access net
access net
… and regional networks may arise to connect access nets to ISPS
ISP B
ISP A
ISP C
IXP
IXP
net
access net
access net
regional net
access net
access net
access net
access net

## Slide 60: Internet structure: network of networks
access net
access net
access
access net
access net
access net
access net
access net
access net
access net
… and content provider networks (e.g., Google, Microsoft, Akamai ) may run their own network, to bring services, content close to end users
ISP B
ISP A
ISP B
IXP
IXP
Content provider network
net
access net
access net
regional net
access net
access net
access net
access net

## Slide 61: Internet structure: network of networks
61
at center: small # of well-connected large networks
“tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national &
international coverage
content provider network (e.g, Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
Regional ISP
Regional ISP
IX
P
IX
P
Tier 1 ISP
Tier 1 ISP
Google
IX
P

## Slide 62: Chapter 1: roadmap
  what is the Internet?
  network edge
    end systems, access networks, links
  network core
    packet switching, circuit switching, network structure
  delay, loss, throughput in networks
  protocol layers, service models
  networks under attack: security
  history

## Slide 63: Host: sends packets of data
host sending function:
takes application message
breaks into smaller chunks, known as packets, of length L bits
transmits packet into access network at transmission rate R
link transmission rate, aka link capacity, aka link bandwidth
R: link transmission rate
host
2 1
two packets,
L bits each
packet transmission
delay
time needed to transmit L-bit packet into link
L (bits)
R (bits/sec)
=
=

## Slide 64: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link (temporarily) exceeds output link capacity
packets queue, wait for turn
packet being transmitted (delay)
A
B
packets queueing (delay)
free (available) buffers: arriving packets dropped (loss) if no free buffers

## Slide 65: Four sources of packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
A
B
propagation
transmission
nodal processing
queueing
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
dtotal = dproc + dqueue + dtrans + dprop

## Slide 66: Four sources of packet delay
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed in medium (~2x108 m/sec)
dprop = d/s
dtrans and dprop very different
propagation
nodal processing
queueing
dtotal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 67: Caravan analogy
10 cars “propagate” at 100 km/hr
toll booth takes 12 sec to service car (bit transmission time)
car~bit; caravan ~ packet
Q: How long until caravan is lined up before 2nd toll booth?
time to “push” entire caravan through toll booth onto highway = 12*10 = 120 sec
time for last car to propagate from 1st to 2nd toll both: 100km/(100km/hr)= 1 hr
A: 62 minutes
toll
booth
toll
booth
ten-car caravan
100 km
100 km

## Slide 68: Caravan analogy (more)
suppose cars now “propagate” at 1000 km/hr
and suppose toll booth now takes one min to service a car
Q: Will cars arrive to 2nd booth before all cars serviced at first booth?
  A: Yes! after 7 min, 1st car arrives at second booth; three cars still at 1st booth.
toll
booth
toll
booth
ten-car caravan
100 km
100 km

## Slide 69: Queueing delay (revisited)
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
traffic intensity
= La/R
La/R ~ 0: avg. queueing delay small
La/R -> 1: avg. queueing delay large
La/R > 1: more “work” arriving
than can be serviced, average delay infinite!
La/R ~ 0
La/R -> 1

## Slide 70: “Real” Internet delays and routes
what do “real” Internet delay & loss look like?
traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 71: “Real” Internet delays, routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic link

## Slide 72: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
packet arriving to full queue dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not at all
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer (waiting area)

## Slide 73: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with file of F bits
to send to client
link capacity Rs bits/sec
link capacity Rc bits/sec
server sends bits (fluid) into pipe
pipe that can carry fluid at rate
Rs bits/sec)
pipe that can carry fluid at rate
Rc bits/sec)

## Slide 74: Throughput (more)
Rs < Rc
What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc
What is average end-end throughput?
bottleneck link
link on end-end path that constrains end-end throughput
Rs bits/sec
Rc bits/sec

## Slide 75: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
R
c
Rc
R
c
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or
R is often
s
bottleneck

## Slide 76: Chapter 1: roadmap
  what is the Internet?
  network edge
    end systems, access networks, links
  network core
    packet switching, circuit switching, network structure
  delay, loss, throughput in networks
  protocol layers, service models
  networks under attack: security
  history

## Slide 77: Protocol “layers”
Networks are complex,
with many “pieces”:
hosts
routers
links of various media
applications
protocols
hardware, software
Question:
is there any hope of organizing structure of network?

## Slide 78: Organization of air travel
a series of steps
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing

## Slide 79: Layering of airline functionality
ticket (purchase)
baggage (check)
gates (load)
runway (takeoff)
airplane routing
departure airport
arrival airport
airplane routing airplane routing
intermediate air-traffic control centers
ticket (complain)
baggage (claim
gates (unload)
runway (land)
airplane routing
ticket
baggage
gate
takeoff/landing
airplane routing
layers: each layer implements a service
via its own internal-layer actions
relying on services provided by layer below

## Slide 80: Why layering?
Dealing with complex systems:
explicit structure allows identification, relationship of complex system’s pieces
  layered reference model for discussion
modularization eases maintenance, updating of
system
  change of implementation of layer’s service transparent to rest of system
  e.g., change in gate procedure doesn’t affect rest of system
layering considered harmful?

## Slide 81: OSI Model
ISO (International standard Organization) tổ chức tiêu chuẩn hóa Quốc tế đề xuất mô hình tham chiếu cho việc kết nối các hệ thống mở (Open System Interconnection -OSI model) (It was first introduced in the late 1970s).
An open system is a model that allows any two different systems to communicate regardless of their underlying architecture (hardware or software).
The OSI model is not a protocol; it is model for understanding and designing a network architecture that is flexible, robust and interoperable.

## Slide 82: OSI Model
The OSI model is a layered framework for the design of network systems that allows for communication across all types of computer systems.
The OSI model is built of seven ordered layers:
(layer 1) physical layer
(layer 2) data link
(layer 3) network layer
(layer 4) transport layer
(layer 5) session layer
(layer 6) presentation layer
(layer 7) application layer

## Slide 83: OSI Model
Layer x on one machine communicates with layer x on
another machine - called Peer-to-Peer Processes.
Interfaces between Layers
Each interface defines what information and services a layer must provide for the layer above it
Organizations of the layers
  Network support layers : Layers 1, 2, 3
  User support layer : Layer 5, 6, 7
    It allows interoperability among unrelated software systems
  Transport layer (Layer 4) : links the two subgroups

## Slide 84: OSI Model

## Slide 85: OSI Model
The data portion of a packet at level N-1 carries the whole packet from level N. – The concept is called encapsulation.

## Slide 86: Internet Model (TCP/IP)

## Slide 87: Physical Layer
The physical layer coordinates the functions required to transmit a bit stream over a physical medium. It also defines the procedures and functions that physical devices and interfaces have to perform for transmission occur.
The physical layer is responsible for transmitting individual bits from one node to the next.

## Slide 88: Physical Layer
The physical layer is concerned with the following:
Physical characteristics of interfaces and media: The physical layer defines the characteristics of the interface between devices and the transmission media, including its type.
Representation of the bits: the physical layer data consist of a stream of bits without any interpretation. To be transmitted, bits must be encoded into signals – electrical or optical-. The physical layer defines the type of encoding.
Data rate: The physical layer defines the transmission rate, the number of bits sent each second.
Line configuration: the physical layer is concerned with the connection of devices to the medium.
Physical topology
Transmission Mode

## Slide 89: Data Link Layer
The data link layer transforms the physical layer, a raw transmission facility, to a reliable link and is responsible for node- to-node delivery. It makes the physical layer appear error free to the upper layer (network layer).
The data link layer is responsible for transmitting frames from one hop (node) to the next.

## Slide 90: Data Link Layer
Hop-to-hop (node-to-node) delivery

## Slide 91: Data Link Layer
Functions of the data link layer:
Framing. The data link layer divides the stream of bits received from the network layer into data units called frames.
Physical addressing. If frames are to be distributed to different systems on the network, the data link layer adds a header to the frame to define the physical address of the sender (source address) and/or receiver (destination address) of the frame.
If the frame is intended for a system outside the sender’s network, the receiver address is the address of the device that connects one network to the next.

## Slide 92: Data Link Layer
Flow Control. If the rate at which the data are absorbed by the receiver is less than the rate produced in the sender, the data link layer imposes a flow control mechanism to prevent overwhelming the receiver.
Error control. The data link layer adds reliability to the physical layer by adding mechanisms to detect and retransmit damaged or lost frames. Error control is normally achieved through a trailer to the end of the frame.
Access Control. When two or more devices are connected to the same link, data link layer protocols are necessary to determine which device has control over the link at any time.

## Slide 93: Network Layer
The Network layer is responsible for the source-to-destination delivery of a packet possible across multiple networks.
If two systems are connected to the same link, there is usually no need for a network layer. However, if the two systems are attached to different networks, there is often a need for the network layer to accomplish source-to-destination delivery.

## Slide 94: Network Layer
Source-to-destination delivery: The network layer is responsible for the delivery of packets from the original source to the final destination.

## Slide 95: Network Layer
Functions of the Network Layer
Logical addressing. The physical addressing implemented by the data link layer handles the addressing problem locally.
The network layer adds a header to the packet coming from the upper layer, among other things, includes the logical address of the sender and receiver.
Routing: When independent networks or links are connected together to create an internetwork (a network of networks) or a large network, the connecting devices (called routers or gateways) route or switch the packets to their final destination.

## Slide 96: Transport Layer
The transport layer is responsible for process-to- process delivery of the entire message.
The network layer oversees host-to-destination delivery of individual packets, it does not recognize any relationship between those packets.
The transport layer ensures that the whole message arrives intact and in order, overseeing both error control and flow control at the process-to-process level.

## Slide 97: Transport Layer
The transport layer is responsible for delivery of a message from one process to another.

## Slide 98: Transport Layer
Functions of the transport layer
  Port addressing: computer often run several processes (running programs) at the same time. Process-to-process delivery means delivery from a specific process on one computer to a specific process on the other.
  The transport layer header include a type of address called port address.
  The network layer gets each packet to the correct computer; the transport
layer gets the entire message to the correct process on that computer.

## Slide 99: Transport Layer
Functions of the transport layer
  Segmentation and reassembly: a message is divided into transmittable segments, each having a sequence number. These numbers enable the transport layer to reassemble the message correctly upon arrival at the destination.
  Connection control: The transport layer can be either
connectionless or connection-oriented.
  A connectionless transport layer treats each segment as an independent packet and delivers it to the transport layer at the destination machine.
  A connection-oriented transport layer makes a connection with the transport layer at the destination machine first before delivering the packets. After all the data are transferred, the connection is terminated.

## Slide 100: Transport Layer
Functions of the transport layer
  Flow control: the transport layer performs a flow control end to end. The data link layer performs flow control across a single link.
  Error control: the transport layer performs error control end to end. The data link layer performs control across a single link.

## Slide 101: Session Layer
The session layer is the network dialog controller. It was designed to establish, maintain, and synchronize the interaction between communicating devices.

## Slide 102: Presentation Layer
The presentation layer was designed to handle the syntax and semantics of the information exchanged between the two systems. It was designed for data translation, encryption, decryption, and compression.

## Slide 103: Application Layer
The application layer enables the user to access the network. It provides user interfaces and support for services such electronic email, remote file access, WWW, and so on.

## Slide 104: Internet protocol stack
application: supporting network applications
  FTP, SMTP, HTTP
transport: process-process data transfer
  TCP, UDP
network: routing of datagrams from source to destination
  IP, routing protocols
link: data transfer between neighboring network elements
  Ethernet, 802.11 (WiFi), PPP
physical: bits “on the wire”
application
transport
network
link
physical

## Slide 105: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression, machine- specific conventions
session: synchronization, checkpointing, recovery of data exchange
Internet stack “missing” these layers!
  these services, if needed, must be
implemented in application
  needed?
application
presentation
session
transport
network
link
physical

## Slide 106: Encapsulation
source
application
transport
network
link
physical
Hn
segment
Ht
datagram
destination
application
transport
network
link
physical
 |  | Ht | M
 | Hn | Ht | M
Hl | Hn | Ht | M
M
network
link
physical
link
physical
 | Hn | Ht | M
Hl | Hn | Ht | M
Ht
Hn
M
router
switch
message
M
Ht
M
 | Hn | Ht | M
Hl | Hn | Ht | M
frame

## Slide 107: Summary of Layer’s Duties

## Slide 108: IEEE 802

## Slide 109: Chapter 1: roadmap
  what is the Internet?
  network edge
    end systems, access networks, links
  network core
    packet switching, circuit switching, network structure
  delay, loss, throughput in networks
  protocol layers, service models
  networks under attack: security
  history

## Slide 110: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks
Internet not originally designed with (much)
security in mind
  original vision: “a group of mutually trusting users attached to a transparent network” 
  Internet protocol designers playing “catch-up”
  security considerations in all layers!

## Slide 111: Bad guys: put malware into hosts via Internet
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed
spyware malware can record keystrokes, web sites visited, upload info to collection site
infected host can be enrolled in botnet, used for spam. DDoS attacks

## Slide 112: Bad guys: attack server, network infrastructure
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
select target
break into hosts around the network (see botnet)
send packets to target from compromised hosts

## Slide 113: Bad guys can sniff packets
packet “sniffing”:
broadcast media (shared ethernet, wireless)
promiscuous network interface reads/records all packets (e.g., including passwords!) passing by
A
C
src:B dest:A
payload
B
wireshark software used for packet-sniffer

## Slide 114: Bad guys can use fake addresses
IP spoofing: send packet with false source address
A
B
C
src:B
dest:A
payload

## Slide 115: Chapter 1: roadmap
  what is the Internet?
  network edge
    end systems, access networks, links
  network core
    packet switching, circuit switching, network structure
  delay, loss, throughput in networks
  protocol layers, service models
  networks under attack: security
  history

## Slide 116: Internet history
Bắt đầu từ một thí nghiệm của dự án của ARPA
Một liên kết giữa hai nút mạng (IMP tại UCLA và IMP tại SRI).
□ | ARPA: | Advanced Research Project Agency
□ | UCLA: | University California Los Angeles
□ | SRI: | Stanford Research Institute
□ | IMP: | Interface Message Processor

## Slide 117: Internet history
3 tháng sau: một mạng hoàn chỉnh với 4 nút, 56kbps
UTAH
SRI
UCSB UCLA

## Slide 118: Internet history
ARPANET thời kỳ đầu, 1971: tốc độ phát triển 1 nút/tháng

## Slide 119: Internet history
Sự mở rộng của ARPANET, 1974: vượt quá 3.000.000 gói tin/ngày

## Slide 120: Internet history
Thập niên 1970:
  Từ đầu 1970 xuất hiện các mạng riêng:
ALOHAnet tại Hawaii
DECnet, IBM SNA, XNA
  1974: Cerf & Kahn – nguyên lý kết nối các hệ thống mở (Turing Awards)
  1976: Ethernet, Xerox PARC

## Slide 121: Internet history
1981: Xây dựng mạng NSFNET
NSF: National Science Foundation: Phục vụ cho nghiên cứu khoa học, do sự quá tải của ARPANET

## Slide 122: Internet history
1986: Nối kết USENET& NSFNET

## Slide 123: Internet history
123
Thêm nhiều mạng mới nối vào: MFENET, HEPNET (Dept. Energy), SPAN (NASA), BITnet, CSnet, NSFnet, Minitel …
TCP/IP được chuẩn hóa và phổ biến vào 1980
Berkeley tích hợp TCP/IP vào BSD Unix
Dịch vụ: FTP, Mail, DNS …
Cuối 1990’s – 2000’s:
Thập niên 90: Web và thương mại hóa Internet
Đầu 90: ARPAnet chỉ là một phần của Internet
Đầu 90: Web
  HTML, HTTP: Berners-Lee
  1994: Mosaic, Netscape
Cuối 90: Thương mại hóa Internet
Nhiều ứng dụng mới: chat, chia
sẻ file P2P…
E-commerce, Yahoo, Amazon, Google…
> 50 triệu máy trạm, > 100 triệu NSD
Vấn đề an toàn an ninh thông tin!
Internet dành cho tất cả mọi người
Tất cả các dịch vụ phải quan tâm tới vấn đề này

## Slide 124: Internet history
2005-present
~750 million hosts
  Smartphones and tablets
Aggressive deployment of broadband access
Increasing ubiquity of high-speed wireless access
Emergence of online social networks:
  Facebook: soon one billion users
Service providers (Google, Microsoft) create their own networks
  Bypass Internet, providing “instantaneous” access to search, emai, etc.
E-commerce, universities, enterprises running their services in
“cloud” (eg, Amazon EC2)

## Slide 125: Internet history
Phát triển Internet ở Việt Nam
https://vi.wikipedia.org/wiki/Internet_tại_Việt_Nam

## Slide 126: Internet history
Thị phần thuê bao dịch vụ truy cập Internet của các doanh nghiệp (tính đến tháng 12/2010)

## Slide 127: Introduction: summary
covered a “ton” of material!
Internet overview
what’s a protocol?
network edge, core, access network
  packet-switching versus circuit-switching
  Internet structure
performance: loss, delay, throughput
layering, service models
security
history
you now have:
context, overview, “feel” of networking
more depth, detail to follow!